## Slide 1: The TinyTol optical system and grading cadence

## Slide 2: Optical system
Chip specifications:
  Pixel size: 1.12μm x 1.12μm
  Chip dimensions: 3280 x 2464 pixels
Optical specifications:
  Folded optical system
  150mm focal length lens
  18mm aperture
  Pupil mounted at a 5.8° angle to lens
Spectral response

## Slide 3: Grating cadence
Each pixel on the detector translates to 1.540 arcseconds
Wanting our sidelobes to reach out to at most 90% of the chip (~1100 pixels from the center) gives us a diffraction angle of 1694 arcseconds
Using the grating equation with values:
  n = 1
  λ = 675 nm
  𝜗 = 8.2127 mrad
This gives us a grating cadence of ~ 82.2μm